Customize Function Specification
3D Robotics
V 1.6
By: Hector Su

## Version History
History
Date	Rev.	Author	Description
2010/05/17	1.0	Hector Su	First Release
2010/05/18	1.1	Hector Su	Second Release
2010/07/08	1.2	Hector Su	Third Release
2010/07/27	1.3	Hector Su	Fourth Release
2010/09/01	1.4	Hector Su	Fifth Release.
2010/11/23	1.5	Hector Su	Sixth Release
2010/11/23	1.6	Hector Su	Seventh Release. Please refer to 2.4~2.5

Purpose

It supports custom function for customer。

Provide Function
2.1
It supports to output custom sentence. It provides two modes:
1. Binary Sentence
2. Standard NMEA Sentence (default)
The format is shown in table 1.
2.2
It supports custom command for mode switch
The format is shown in the table 2.
2.3
The system can leave the values with last valid information when user lost satellite reception.
2.4
It changes the preamble header from “0xB5,0x62” to “0xD0,0xDD”. And it removes the item “Class and MSG ID”. Please refer to table 1.
2.5
The format of UTC time, it uses extra two digits for milliseconds. Please refer to table 1.

Customize Data Format Table-1
Name	Example	Units	Description
Preamble	0xD0,0xDD	2 bytes	Preamble header
Payload	0x20	1 byte	The count of item from “Latitude” to “HDOP”
Latitude	0xF9 / 0x8F / 0xC4 / 0x0D	4 bytes / Low byte / to / Hi byte	Latitude (in decimal degrees) / The original value will be converted / Example:23.0985721*(10^7)=230985721
Longitude	0xB8 / 0xF0 / 0xB1 / 0x47	4 bytes / Low byte / to / Hi byte	Longitude (in decimal degrees) / The original value will be converted / Example:120.2843832*(10^7)=1202843832
MSL Altitude	0x9A / 0x0D / 0x00 / 0x00	4 bytes / Low byte / to / Hi byte	MSL Altitude (meter) / The original value will be converted / Example:34.82*(10^2)=3482
Ground Speed	0x09 / 0x00 / 0x00 / 0x00	4 bytes / Low byte / to / Hi byte	Ground Speed(m/s) / The original value will be converted / Example:0.324(km/hr)  0.324*1000/3600 =0.09 (m/s) / 0.09*100=9
Heading	0x18 / 0x30 / 0x00 / 0x00	4 bytes / Low byte / to / Hi byte	Heading(degrees) / The original value will be converted / Example:123.12123.12*(10^2)=12312
Satellites	0x09	1 byte	The value of satellites in viewed
Fix Type	0x03	1 byte	GPS fix type / 0x01  GPS no fix / 0x02  GPS 2D fix / 0x03  GPS 3D fix
Date	0xC6 / 0x86 / 0x03 / 0x00	4 bytes / Low byte / to / Hi byte	DDMMYY / Example:2010/11/23 =>231110
UTC Time	0xF6 / 0x26 / 0x33 / 0x00	4 bytes / Low byte / to / Hi byte	It shows a part of UTC Time Example: 03:35:23.10  33523.10 / 33523.10*(10^2)3352310
HDOP	0x73 / 0x00	2 bytes / Low byte / to / Hi byte	Horizontal Dilution of Precision / Example:1.15  1.15*(10^2)=115
CK_ A	0x47	1 byte	Checksum_A Refer to (1)
CK_B	0xF8	1 byte	Checksum_B Refer to (1)

Customize Command Format Table 2
Name	Example	Units	Description
Message ID	$PGCMD		Customize command header
Command Number	16		This number represents which command is used
Parameter 1:RMC	1		Period of RMC, 0~5. 0 mean to disable output
Parameter 2:VTG	1		Period of VTG, 0~5. 0 mean to disable output
Parameter 3:GSA	1		Period of GSA, 0~5. 0 mean to disable output
Parameter 4:GSV	1		Period of GSV, 0~5. 0 mean to disable output
Parameter 5:GGA	1		Period of GGA, 0~5. 0 mean to disable output
Checksum	*6B
<CR> <LF>			End of message termination

Example：$PGCMD,16,1,1,1,1,1*6B or $PGCMD,16,0,0,0,0,0*6A(2)

Note

1. The checksum CK_A and CK_B. It be calculated from all bytes sent except for the preamble bytes(0xD0),0xDD)
CK_A = 0, CK_B = 0
For(I=0;I<N;I++)
{
      CK_A = CK_A + Buffer[I]
      CK_B = CK_B + CK_A
}

2. This command for mode switching. When user inputs command “$PGCMD,16,0,0,0,0,0*6A”, then switch to binary mode. Otherwise for standard NMEA mode.